## Slide 1
Robot-Collected Field Data and Agent-Run Training for Laser Weeding
Harry He · Hongbo Zhang
Department of Engineering Technology · Middle Tennessee State University, Murfreesboro, TN, USA
Two ground vehicles drive our own crop plots while a pair of agents collect, filter and train on the cluster with nobody in the room. This is what the machines recorded, what the agents did, and the one link between them we have not closed.
Figure 1. Four frames as recorded, unenhanced and unlabelled. The rectangle in (c) is the cart's fixed work-zone overlay. It is drawn on every frame, including the ones with no vegetation in them.
2,686
camera frames
26 drives, 2 robots
91,955
telemetry rows
nine streams, counted line by line
342 m
of GPS track
1,502 fixes over 18 drives
75
cart frames in a field
of 427 the cart has recorded
0
of them labelled
the whole archive, so far
How a drive becomes a dataset
A vehicle opens a session, the platform registers it as a governed dataset, and frames and sensor batches arrive over one API key while the vehicle is still driving. Robot 241 sends camera, GPS and two IMUs. The laser cart sends camera, laser state, vehicle telemetry and its own detections, and no position at all.
213 seconds in one crop plot
Figure 2. Robot 241, 2026-08-29: one 213 s pass through a crop plot. (h) GPS track from the board fix. (i) IMU heading over the same pass.
What the agents do with it
Figure 3. The path as built, from a camera in a crop row to a checkpoint on the cluster. Every stage has run. Three qualifications ride on it. The collector and trainer are paused after a stop-loss on 2026-08-29. The supervisor is advisory and nothing it says is applied. And the last link is not closed: no robot frame has entered training, because none of them is labelled yet.
We let it run itself for fifteen rounds
Figure 4. (f) Fifteen unattended rounds on a fixed holdout. (g) Round 15's exact dataset, three ways. The first two marks differ only in the starting weights, so their gap is the warm-start chain; the third is the recipe the campaign ran, whose wall-clock cap truncates the cosine, with its three seeds drawn behind it. Sigma throughout is that recipe's own seed spread, 0.0040 over three seeds, propagated to the difference being quoted. Completing the schedule is not the fix -- the second mark sits below the third.
Every round reported success and accuracy fell the whole time. The corpus stopped growing at round three and eight rounds collected nothing. What was left was the chain: starting fresh instead of from the previous round's weights is worth +0.0287, 5.1 times this recipe's own seed spread.
Then we pointed it back at our own rows
Figure 5. The deployable checkpoint over every frame the two robots recorded, at the confidence the cart deploys at. There is no ground truth for these frames, so this is the rate at which the detector produces a box at all -- not recall and not precision. Vegetation is excess green over a thumbnail, so "nothing to detect" does not account for it: 1157 frames clear that bar and 21 of them draw a box. 24 of the 25 boxes it does draw are the same class.
The deployable checkpoint draws a box on 25 of the 2,686 frames our robots recorded, and 24 of those 25 boxes are the same class. These frames carry no labels, so that is a firing rate, not recall and not precision. On a second labelled weed dataset the same checkpoints fall from 0.873 to 0.100.
Does more web data help?
harvested added
mAP50-95
n
none, the core
0.8637 ± 0.0027
3
+5,000
0.8609 ± 0.0036
3
+15,000
0.8580 ± 0.0047
3
+40,000
0.8448 ± 0.0018
3
Twelve times the data costs 0.0189, which is 8.2 times the seed spread, and the same eight checkpoints fall on a second dataset too. One of six audited web sources clears a 0.90 label-precision bar. This is why the robots exist.
Everything we trained, ran, or rejected
Figure 6. 30 rows in four families, which is 27 distinct models: OWLv2-large and Qwen2.5-7B each appear twice because each does two jobs here. One model is deployed. The zero-shot column is a single deterministic pass per model with no repeats, scored as mAP50 on the 848-image split; the reviewer column is the 149-case dev split, and two of its arms are still running. RF-DETR's score is on a third scale and is never differenced against the rows above it: the one measured offset between two of our evaluators, 0.0239, is larger than the gap on display.
Six audited web sources
Of 13,527 labelled images from six audited harvested sources, only 3,208 come from a source that clears a 0.90 label-precision bar. The other five score between 0.18 and 0.74. The same probe reads 1.000 on human-labelled CottonWeedDet12, so those are the data and not the instrument.
Who notices when it breaks
reviewer
recall
grounded
incidents
scripted watchdog
no decision
—
—
12 rules
0.095
0.095
116
Qwen2.5-7B
0.823
0.274
113
Qwen3-14B
0.675
0.614
114
Qwen3.8-27B
0.702
0.702
57
162 real failures out of this project's own record, frozen as a corpus. The watchdog the loop was running returned no decision on any of the 149 dev cases. Recall does not order the reviewers by size; evidence does.
Where this stands today. The collector and trainer are paused after a stop-loss on 2026-08-29 and the last field drive was the same day. The supervisor is advisory. The laser has never fired at a weed under our control.
How the numbers were made. Most in-domain numbers are mAP50-95 on the same 1,977 images under Ultralytics. RF-DETR is pycocotools and the zero-shot column is mAP50 on the 848-image test split; neither is ever differenced against the rest. That holdout is also the validation set during training, so every mAP here is a run's best epoch, a maximum over 21 to 100 evaluations on the set it is reported on.
Numbers we withdrew. 0.910 was a data leak, found by a check we built after publishing it. 0.9033 is the best of four unseeded runs. An earlier reading of the ladder as a flat curve is retracted.