## Slide 1
Two Field Robots and an Agent Platform for Laser Weeding
Harry He · Hongbo Zhang
Department of Engineering Technology · Middle Tennessee State University, Murfreesboro, TN, USA
Anyone can download a weed dataset this afternoon. Nobody can download the path from a robot in a Tennessee crop row to a trained checkpoint, so we built it, ran it unattended, and measured where it breaks.
Figure 1. The path from a camera in a crop row to a checkpoint on the cluster. Every stage is built and has run. Two are not running today: the collector and trainer are paused after a stop-loss on 2026-08-29, and the supervisor is advisory, so nothing it says is applied to the loop.
The two vehicles
Figure 2. Frames as recorded, unenhanced. Robot 241 has sent 2,259 frames at 640 x 360 and 1 Hz, the laser cart 427, and 75 of the cart's were taken in a field. None of the 2,686 is labelled. The rectangle in the down camera is the cart's fixed work-zone overlay. It is drawn on every frame, including the ones with no vegetation in them.
Robot 241 is a tracked rover that drives cotton rows and streams frames, position and attitude over a cellular link. The laser cart carries the weeder itself: a galvanometer laser, a down camera over the work zone and a forward camera. Between them they have recorded 2,686 frames in 26 drives. None is labelled.
What is on disk
2,686
camera frames
26 drives, 2 robots, 0 labelled
91,955
telemetry rows
nine streams: GPS, two IMUs, motor, laser, control
342 m
of GPS track
1,502 fixes over 18 drives; the longest single pass is 141 m
The cart has no position sensor.
Its archive declares four telemetry streams and neither of them is GPS or IMU, so the sensor-fusion work on this platform is robot 241 only.
Why build the path
The end product burns weeds between crop rows instead of spraying them, so the detector has to work on the rows this vehicle drives and has to fit on the Jetson the cart carries. The deployed checkpoint is 2.6 M parameters. No public dataset contains our rows, and a five-person lab does not hand-label a hundred thousand field images.
One drive, in full
Figure 3. Robot 241, 2026-08-29: one 213 s pass through a crop plot. (h) GPS track from the board fix. (i) IMU heading over the same pass.
What the agents did on their own
Two SLURM jobs, one collecting and one training, ran fifteen rounds against the locked registry with nobody in the room. Each round searched public sources, filtered what it found, merged it into the corpus, trained, and evaluated on a sealed holdout. Every round reported success. Accuracy fell for fifteen rounds.
Figure 4. (f) Fifteen unattended rounds on a fixed holdout. (g) Round 15's exact dataset, three ways. The first two marks differ only in the starting weights, so their gap is the warm-start chain; the third is the recipe the campaign ran, whose wall-clock cap truncates the cosine, with its three seeds drawn behind it. Sigma throughout is that recipe's own seed spread, 0.0040 over three seeds, propagated to the difference being quoted. Completing the schedule is not the fix -- the second mark sits below the third.
Reading the loop's own artifacts instead of its dashboard explained it. The training corpus stopped growing at round three: the same 24 datasets and the same 48,752 unique images went in every time, and the apparent growth was one staging directory nobody cleared. Eight rounds collected nothing at all and reported success. What was left was the chain itself, and a control on round 15's own data priced it: starting fresh instead of from the previous round is worth +0.0287, which is 5.1 times the seed spread this recipe actually has.
Does more data help?
harvested added
mAP50-95
n
none, the core
0.8637 ± 0.0027
3
+5,000
0.8609 ± 0.0036
3
+15,000
0.8580 ± 0.0047
3
+40,000
0.8448 ± 0.0018
3
Twelve times the training data costs 0.0189 on our own holdout, which is 8.2 times the seed spread. The same eight checkpoints scored on a second weed dataset fall too, by 0.0299, so this is the data and not the metric. One of six audited web sources reaches a 0.90 label-precision bar, and 44,750 of 156,521 harvested images are copies of each other.
Everything we trained, ran, or rejected
Figure 5. 27 distinct models, in four families, on one holdout or one incident corpus. One of them is deployed. The zero-shot column is a single deterministic pass per model with no repeats; the reviewer column is the 149-case dev split, and two of its arms are still running.
Back on our own rows
Figure 6. The deployable checkpoint over every frame the two robots recorded, at the confidence the cart deploys at. There is no ground truth for these frames, so this is the rate at which the detector produces a box at all -- not recall and not precision. Vegetation is excess green over a thumbnail, so "nothing to detect" does not account for it: 1157 frames clear that bar and 21 of them draw a box. 24 of the 25 boxes it does draw are the same class.
Who notices when it breaks
We froze 162 real failures out of this project's own engineering record and scored every kind of supervision we had against them. The watchdog the loop actually ran returned no decision on any of the 149 dev cases: “no signal fired” is not a judgement. Twelve deterministic checks reach 0.095. A model reading the raw artifacts reaches 0.70, and what separates the models is not size but evidence. The 7 B leaves 55% of its findings unevidenced and the 27 B leaves none.
reviewer
recall
grounded
scripted watchdog
no decision
—
12 rules
0.095
0.095
Qwen2.5-7B
0.823
0.274
Qwen3-14B
0.675
0.614
Qwen3.8-27B
0.702
0.702
Where this stands today. The collector and trainer are paused after a stop-loss on 2026-08-29. The last field drive was the same day. The supervisor is advisory and nothing it says is applied. The laser has never fired at a weed under our control. None of the 2,686 frames is labelled.
How the numbers were made. Every in-domain number is mAP50-95 on the same 1,977 images of CottonWeedDet12 under one evaluator, and that set is also the validation set during training, so each figure is a maximum over many evaluations. We measured that optimism at +0.002 to +0.017 rather than hiding it, and every conclusion here survives re-reading at last epoch.
Numbers we withdrew. 0.910 was a data leak, found by a content-level check we built after publishing it. 0.9033 is the best of four unseeded runs and only one of the four crossed 0.90. An earlier reading of the ladder as a flat curve is retracted: with three seeds at every rung the top rung is down, not flat.