## Slide 1
agentAI: A Research-Data Platform for Physical and Embodied Agents
Harry He · Hongbo Zhang
Department of Engineering Technology · Middle Tennessee State University, Murfreesboro, TN, USA
Built at the MTSU Great Robotics Lab. Every robot the lab owns reports into one platform; agents on it harvest, filter, label and train; a third agent watches the other two. This is what runs today, what the robots have recorded, and what six months of running it taught us.
2,686
camera frames
26 drives, 2 robots, 0 labelled
91,955
telemetry rows
nine streams, counted line by line
342 m
of GPS track
1,502 fixes over 18 drives
27
distinct models run
four families, one deployed
0
robot frames labelled
the whole archive, so far
One platform for every robot the lab owns
agentAI is a research-data platform for physical and embodied agents, built at the MTSU Great Robotics Lab. A robot, a drone or a sensor rig is a project. A project owns its keys, its people and a locked dataset registry. Agents on the platform harvest, filter, label and train against that registry. Adding a robot is a configuration, not a migration.
1,389
joystick commands through the platform
Driving a robot from a browser
A signed-in user opens the 241 project and clicks Drive. The platform reverse-proxies the robot's own console over the lab tailnet, so the rover is driven from a plain browser with no VPN client. 1,389 joystick commands have gone through that path. Two gates sit in front of it: the platform's Google login, then the robot's own password.
On disk today
Two robots have put 2,686 camera frames and 91,955 telemetry rows across nine streams onto the platform, over 26 drives, with 342 m of GPS track from 1,502 fixes. None of the frames is labelled.
92
questions asked of a dataset so far
Asked something it had never seen
Asked to plot a histogram of the heading change rate on the 241 field drive, the agent wrote the code and returned the plot on the first attempt. A fixed template cannot do that, because nothing in the platform knew that question would be asked. Across the platform, 9 datasets carry 92 turns of that conversation.
More web data, less accuracy
Twelve times the training data costs 0.0189 on our own 1,977-image holdout, three seeds at every rung, which is 8.2 times the seed spread. The same eight checkpoints fall on a second weed dataset too. One of six audited web sources reaches a 0.90 label-precision bar.
Adding the next robot
A new robot needs a project, an API key and a session start. The ingest contract is the same for every vehicle: open a session, post sensor batches and frames while driving, stop. The platform does not care what the robot is. Empty projects for a mobile robot and a humanoid already sit on it, waiting for a first upload.
Code the agent writes runs fenced in
Generated code passes an import whitelist and an AST check before it runs, with no network and no file writes, 15 seconds of CPU, 1.5 GB of memory and a 25 second wall clock. A user can edit the agent's code or paste their own and re-run it in the same fence.
Robots on the platform today
Robot 241 is a tracked rover that drives crop rows and streams camera, GPS and two IMUs. The laser cart carries the weeder: a galvanometer laser, a down camera over the work zone and a forward camera. Ten projects sit on the platform and two of them have a robot reporting into them. Between those two vehicles, 2,686 frames in 26 drives.
14
analysis tools the planner can choose from
Ask a dataset what it is good for
Every dataset page carries a chat box. A user types or speaks a plain question about that dataset. A planner reads the question and the dataset's real column profile, then picks from 14 fixed analysis tools or writes new code. The answer comes back with the chart and the code that produced it.
Left alone for fifteen rounds
Figure 1. (f) Fifteen unattended rounds on a fixed holdout. (g) Round 15's exact dataset, three ways. The first two marks differ only in the starting weights, so their gap is the warm-start chain; the third is the recipe the campaign ran, whose wall-clock cap truncates the cosine, with its three seeds drawn behind it. Sigma throughout is that recipe's own seed spread, 0.0040 over three seeds, propagated to the difference being quoted. Completing the schedule is not the fix -- the second mark sits below the third.
Two cluster jobs, one collecting and one training, ran fifteen rounds against the locked registry with nobody in the room. Each round searched public sources, filtered what it found, merged, trained and evaluated. Every round reported success. Accuracy fell for fifteen rounds. This part is built and is switched off today.
27
distinct models trained, run, or rejected
Everything we trained, ran, or rejected
Figure 2. 30 rows in four families, which is 27 distinct models: OWLv2-large and Qwen2.5-7B each appear twice because each does two jobs here. One model is deployed. The zero-shot column is a single deterministic pass per model with no repeats, scored as mAP50 on the 848-image split; the reviewer column is the 149-case dev split, and two of its arms are still running. RF-DETR's score is on a third scale and is never differenced against the rows above it: the one measured offset between two of our evaluators, 0.0239, is larger than the gap on display.
Thirty rows in four families, which is 27 distinct models. Five detectors trained on our own holdout, two vision models inside the loop, fourteen vision-language models zero-shot, and nine language models as reviewers. One is deployed.
A drive becomes a dataset as it opens
A vehicle opens a session and the platform registers it as a governed dataset at that moment, not after the drive ends. Frames and sensor batches arrive over one API key. Robot 241 sends camera, GPS and two IMUs; the laser cart sends camera, laser state, vehicle telemetry and its own detections, and no position at all.
Four frames, as recorded
Figure 3. Frames as recorded, unenhanced. Robot 241 has sent 2,238 frames at 640 x 360 and 1 Hz, the laser cart 427, and 75 of the cart's were taken in a field. None of the 2,686 is labelled. The rectangle in the down camera is the cart's fixed work-zone overlay. It is drawn on every frame, including the ones with no vegetation in them.
Nothing here is enhanced and nothing is labelled. The rectangle in the cart's down camera is a fixed work-zone overlay: it sits at the same pixels on frames with no vegetation in them at all.
Only one robot has the button
The Drive button appears on the 241 project and not on the laser cart's, because the allow-list holds one target. The rover has been dark since 2026-08-28: the platform answers a drive request today with its own offline page. The cart has never been drivable from the platform.
Which decisions a model makes
A language model decides what the collector goes after next, judges whether a candidate dataset is on topic, and reviews a finished step. Those run on the cluster, as batch jobs, on open weights. The lab box hosts only the small guide model, and a verdict produced there is marked in its own record as a draft that may not be reported.
Any research field is a project
A lab member opens a project for any data type and any field, uploads images, video or sensor logs, and gets an automatic diagnosis before choosing what to do next. Weed detection is one project on this platform. The 241 rover, the laser cart and a Unitree humanoid each have their own.
Standing today. The collector and trainer are paused after a stop-loss on 2026-08-29. The rover has been off the tailnet since then and the platform answers a drive request with its offline page. The supervisor is advisory. None of the 2,686 frames is labelled.
How the numbers were made. Most in-domain numbers are mAP50-95 on the same 1,977 images under Ultralytics. RF-DETR is pycocotools and the zero-shot column is mAP50 on the 848-image split; neither is differenced against the rest. That holdout is also the validation set during training, so every mAP here is a run's best epoch.
Numbers we withdrew. 0.910 was a data leak, found by a content-level check we built after publishing it. 0.9033 is the best of four unseeded runs and only one of the four crossed 0.90. An earlier reading of the ladder as a flat curve is retracted.